# DYMEC SERIAL LINKS: KY-MWF208-F

# 8 Channel Serial to Fiber Multiplexer

# Product Description

The KY-MWF208 Multi-channel data multiplexing optical transceiver can provide multi-channel RS-232 / RS-485 / RS-422 transmissions over one optical fiber link. This not only saves fiber resources, but also uses optical fiber as transmission medium to opto-isolate high voltages and prevent electromagnetic interference. ,and anti-lightning. Widely used in various industrial controls and electrical switchgear. Also widely used in the field of industrial automation, especially suitable for power system automation, traffic control and factory automation, including power wind farms.

Features:

- RS-232 / RS-422 / RS-485 conversion, full/half-duplex communications.

- Signal flow is automatically identified and transparently transmitted.

- Optical transceiver module to ensure a reliable transmission distance along with Opto-isolation.

- Unique serial protection circuit, hot-swappable.

- Industrial grade design and all surface mount processes ensure the long-term reliability of the product.

- Genuine DYMEC

# Product Specifications

| Technical parameters |
| --- |
| Standard | Compliant with EIA RS-232, RS-485, RS-422 |
| Interface |
| Interface form | Serial Port: Electrical characteristics, Meet RS-232 / RS-422 / RS-485 Physical characteristics, RJ-45 port Optical interface: Single multi-mode optional, SC/ST/FC optional |
| Communication rate |
| Baud Rate | 300bps~115.2Kbps, rate fully adaptive signal |
| LEDs |
| Power indicator | POW |
| Data transmission indicator lights | TXD, RXD, TX1-TX8, RX1-RX8, ERR (KY-MWF208-F) |
| Power |
| Power Supply | DC5~12V |
| Interface | P1J coaxial input |
| Power | <5W |
| Overload protection | Supported |
| Lightning protection | 600W/ms anti-lightning strike |
| Static protection | 15kv anti-static |
| Physical Characteristics |
| Shell | Military Grade Aluminum housing |
| Dimensions | 225mm×28mm×96mm (KY-MWF208 M/S) |
| Transmission distance |
| Serial port line | RS-232, 15m@9600bps RS-422 / RS-485, 1.2km@9600bps |
| Multi-mode fiber | 1310nm, 2Km |
| Single mode fiber | 1310nm, 20Km / 40Km 1550nm, 60Km / 80Km |
| Working Environment |
| Operating Temperature | -40° ~ +85°C |
| Storage temperature | -40° ~ +85°C |
| Ambient Humidity | 5%~95% |
| Warranty |
| Warranty | 5 Years |
| Certifications |
| Certification | CE, FCC, NEMA TS-2, UL |

# Ordering information

| KY-MWF208-F(M) Multi-Mode Fiber KY-MWF208-F(S) Single-mode Fiber | 8 x RS-232 / RS-485 / RS-422 multi-mode fiber multiplexed optical transceiver, RJ-45 interface type, external DC5~12V, includes standard DC5V/ 1A power adapter, aluminum alloy case for bulkhead installation. 8 x RS-232 / RS-485 / RS-422 single-mode fiber multiplexed optical transceiver, RJ-45 interface type, external DC5~12V, includes standard DC5V/ 1A power adapter, aluminum alloy case for bulkhead installation. Specify Fiber Distance Needed: 20Km / 40Km / 60Km or 80Km |
| --- | --- |