# DY-5844MA-ST

# RS232/RS485/RS422 Serial to Fiber Converter

# PRODUCT DESCRIPTION

The primary functionality of the DY-5844MA-ST Serial Link (photoelectric / fiber converter) is to realize the photoelectric conversion of RS-232/RS-485/422 signals. This series of products realizes long-distance transmission through RS-232 or RS-485 or RS-422 through optical fiber. Optical fiber converters use optical fiber as the transmission medium, having the advantages of isolation high voltage, anti-electromagnetic interference, and anti-lightning. Widely used in various industrial controls, distributed data acquisition and other applications. The devices are especially suitable for power system automation, traffic control and switch gear.

Features:

- RS-232/RS-485 / RS-422 interfaces.

- Small Form Factor – Reduced footprint size.

- Complete Kit – includes converter, AC power supply if needed, and DB-9 Cable

- ST Fiber Connectors

- Opto Isolation

- Lightning Protection

- Signal flow is automatically identified and transparently transmitted.

- High gain optical transceiver module to ensure the transmission distance and quality.

- The baud rate automatically adapts without changing the user protocol.

- Industrial design, all surface mount technology, extended MTBF.

| Technical Specifications |
| --- |
| Standard | Compliant with EIA RS-232, RS-485, RS-422 Protocols |
| Interface |
| Interface formats | Serial Port: Electrical characteristics, Meet RS-232/RS-422/RS-485 Physical characteristics, Industrial terminal block Optical interface: Single multi-mode optional, SC/ST/FC optional |
| Communication Rate |
| Baud Rate | 300bps~115.2Kbps, rate adaptive signal |
| LEDs |
| Power indicator | POW |
| Data transmission indicator lights | TX, RX |
| Power |
| Power Supply | 5 – 36 Volts DC, BNC coaxial input, industrial terminal block |
| Power | <1W |
| Overload protection | Supported |
| Lightning protection | 600W/ms anti-lightning strike |
| Static protection | 15kv anti-static |
| Physical Characteristics |
| Shell | Military Grade - Aluminum housing / bulkhead – wall mount installation |
| Dimensions (W x H x D) | 78 × 25 × 85 mm (Small Form Factor) |
| Transmission Distance |
| Serial port line | RS-232, 15m@9600bps /// RS-422/RS-485, 1.2km@9600bps |
| Multi-mode fiber | 850nm/1310nm,2Km |
| Single mode fiber | 1310nm, 20km/40km /// 1550nm, 60km/80km |
| Working Environment / Temperature Range |
| Operating Temperature | -40°C~85°C |
| Storage temperature | -40°C~85°C |
| Ambient Humidity | 5%~95% |
| Warranty |
| Warranty | 5 Years |
| Certifications |
| Certifications | CE, FCC, UL, NEMA TS2 / IEEE1613 / IEC61000-6-5 (IEC61850-3) UL, CE, FCC, IEEE, IEC, ITUT, NEMA, Substation & Digital Substation, Switchgear IEEE 61850-3 Used in Electrical Substations & Distribution IEEE 1613 Used in Electrical Substations & Distribution EN50155 Used in Railway & Transportation EN50121-4 Used in Railway & Transportation NEMA TS-2 – Used in Traffic Signal Control Systems |

# ORDERING INFORMATION

| DY-5844MA-ST | COMPLETE KIT 1. RS232 / 485 / 422 three-in-one terminal interface fiber converter / Opto Isolating / Serial Link. (Small Form Factor) 2. Multi-mode Fiber 2KM, ST fiber connector (SC or FC connector are available). 850nm 3. External Wall Mount AC to 5~36 Volts DC power supply. 4. DB-9 Cable. (Male to Female) |
| --- | --- |
| DY-5844SA-ST | COMPLETE KIT 1. RS232 / 485 / 422 three-in-one terminal interface fiber converter / Opto Isolating / Serial Link. (Small Form Factor) 2. Single-mode Fiber 20KM, (40km/60km/80km are available); SC, (ST or FC connectors are available.) 1310nm 3. External Wall Mount AC to 5~36 Volts DC power supply. 4. DB-9 Cable (Male to Female) |